## Slide 1
Why accelerators?
1 Institute of Computer Science, Foundation for Research and Technology - Hellas, Greece
2 Computer Science Department, University of Crete, Greece
manospavl@ics.forth.gr
Antonis Chazapis1
Manos Pavlidakis1,2
chazapis@ics.forth.gr

## Slide 2: What is an accelerator?
All about accelerators
EuroHPC 2021
A device that performs some functions more efficiently than general-purpose CPU
CPUs have to be good at all functions
E.G. GPUs are perfect for M.M.
Programming Guide :: CUDA Toolkit Documentation (nvidia.com)

## Slide 3: Typical accelerators
All about accelerators
EuroHPC 2021
All about accelerators
GPGPUs General Purpose Graphic Processing Unit (NVIDIA, AMD)
FPGA: Field-programmable gate array (Xilinx, Intel Altera)
ASIC: Application-Specific Integrated Circuit
  TPU: Tensor Processing Unit (Google)
Accelerators fit perfectly to accelerate compute intensive applications as:
  Financial
  Face detection
  Autonomous driving
  Language translation
  Genomics

## Slide 4: Why accelerators are better than CPUs?
All about accelerators
EuroHPC 2021
Accelerators can process data several orders of magnitude faster than CPUs
  Due to massive parallelism
CPU | GPU
Central Processing Unit | Graphics Processing Unit
Several Cores | Many Cores
Complex/Larger cores | Simpler/smaller cores
Low latency | High throughput
Good for serial processing | Good for parallel processing
Good for almost all operations | Perfect for some operations

## Slide 5: How to select the optimal accelerator?
All about accelerators
EuroHPC 2021
Application type | Processing speed | Processing/ Watt | Training | Inference
Speech processing | ++ | ++ | GPU, ASIC | CPU, ASIC
Face detection | ++ | ++ | GPU, FPGA | CPU, ASIC
Financial risk stratification | ++ | + | GPU, FPGA | CPU
Route planning | + | + | GPU | CPU
Dynamic pricing | ++ | + | GPU | CPU, ASIC
Autonomous driving | ++ | ++ | ASIC | GPU, ASIC, FPGA
https://www.mckinsey.com/industries/semiconductors/our-insights/artificial-intelligence-hardware-new-opportunities-for-semiconductor-companies#
Notes: Since each use case has different compute requirements, the optimal AI hardware architecture will vary. For instance, route-planning applications have different needs for processing speed, and other performance features than applications for autonomous driving or financial risk stratification
https://inaccel.com/cpu-gpu-fpga-or-tpu-which-one-to-choose-for-my-machine-learning-training/
https://inaccel.com/cpu-gpu-or-fpga-performance-evaluation-of-cloud-computing-platforms-for-machine-learning-training/

## Slide 6: Preferred architectures are shifting!
All about accelerators
EuroHPC 2021
https://www.mckinsey.com/industries/semiconductors/our-insights/artificial-intelligence-hardware-new-opportunities-for-semiconductor-companies#

## Slide 7: How to use an accelerator?
All about accelerators
EuroHPC 2021
Use the accelerator programming language and libraries
  CUDA  NVIDIA GPUs, OpenCL  Intel Altera FPGAs
  cuDNN, cuBLAS  NVIDIA GPUs, clBLAS  Intel Altera FPGAs
Generic Programming languages
  OneAPI, OpenCL
High level languages
  Python, Java
  For instance CUDA offers plugins for high-level languages (PyCUDA, JCUDA)
Frameworks
  TensorFlow, PyTorch, MatLab, Caffe, Wolfram Language, mxnet etc.
  Have implementations for different accelerator types
  Have simple and flexible APIs that simplify their use (e.g. Keras)

## Slide 8: Machine learning stack
All about accelerators
EuroHPC 2021
Keras
TensorFlow
Theano
CNTK
PyTorch
CUDA, cuDNN
BLAS, Eigen
GPU
CPU
FPGA
Low-level lib:
Backend:
Hardware:

## Slide 9: MLPerf Data-center benchmarks
All about accelerators
EuroHPC 2021
Chart: Performance improvement (x)
| Image Classification (ResNet-50) | Object Detection (SSD-Large) | Medical Imaging (3D U-Net) | Recommendation (DLRM) | Speech Recognition(RNN-T) | NLP (BERT)
Intel Cooper Lake | 0.1 | 0.1 | 0.1 | 0.001 | 0.005 | 0
Intel Ice Lake | 0.2 | 0.2 | 0.2 | 0 | 0 | 0.2
Xilinx VCK5000 | 0.5 | 0 | 0 | 0 | 0 | 0
Qualcom AI 100 | 1.5 | 1.5 | 0 | 0 | 0 | 0
NVIDIA A100 | 3 | 3 | 2.8 | 3.2 | 2.9 | 4
https://inaccel.com/cpu-gpu-or-fpga-performance-evaluation-of-cloud-computing-platforms-for-machine-learning-training/
NA
NA
NA
NA
NA
NA
NA
NA
NA
NA
NA
NA
20x
314x
JETSON XAVIER NX
Notes: https://www.hpcwire.com/2021/04/21/mlperf-issues-new-inferencing-results-adds-power-metrics-nvidia-wins-again/
The results that you see here (below) are normalized to Jetson Xavier NX

## Slide 10
Thank you
Manos Pavlidakis
manospavl@ics.forth.gr
Questions?
Notes: Thank you very much for you attention I will be happy to answer any questions.