## Slide 1
TReM: A Task Revocation Mechanism for GPUs
1 Institute of Computer Science, Foundation for Research and Technology - Hellas, Greece
2 Computer Science Department, University of Crete, Greece
manospavl@ics.forth.gr
mavridis@ics.forth.gr
nchrysos@ics.forth.gr
bilas@ics.forth.gr
Manos Pavlidakis1,2
Stelios Mavridis1
Nikos Chrysos1
Angelos Bilas1,2
Notes: I am a PhD candidate in Computer Science Department, of University of Crete, Greece.

## Slide 2: GPU sharing
Leads to SLA violation
U
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Today, GPUs are offered in a dedicated manner by cloud providers
To ensure SLA for user-facing tasks
  User-facing task’s response time < SLA
But GPUs are underutilized
State of the art approaches increase GPU utilization
By using idle GPUs for batch tasks
  Batch task does not have strict response time requirements
User-facing task can meet its SLA target
But batch tasks execution time ≥ SLA
If batch task execution time adequately < SLA
B
SLA
Time
Time
SLA
B
U
Notes: Today GPUs are offered in a dedicated manner by cloud providers to ensure SLA to user-facing tasks. User-facing task require tail latency guarantees, in particular its response time should be shorter than a Service Level Agreement (SLA). (click)
But GPUs are under-utilized because one application is not always capable to fully utilize a GPU. (click)
State of the art approaches increase GPU utilization by sharing a GPU among user-facing & batch tasks.
A batch task does not have strict response time requirements but its execution can not be postponed for ever. (click)
If the batch task execution time is adequately smaller than the SLA, as you can see in the example on the right side. One can wait for the batch task to finish and then start the user-facing. (click)
And the user facing will meet its SLA target. (click)
However, batch tasks commonly have execution time greater or equal to the SLA. So if we wait for the batch task to finish and then start the user-facing, (click)
This will lead to a SLA violation (click)

## Slide 3: Preemption can reduce SLA violations
GPU preemption approaches incur variable & high latency:
1. Rely on existing thread blocks or slice tasks to provide preemption points
  Rare preemption points  high latency
  Frequent preemption points  increase task execution time
2. Store stopped task’s state
  In GPU memory  memory monopolization
  In Host memory  variable latency
High preemption latency affects violations
Time
SLA
B
Stop signal
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Notes: Preemption can reduce SLA violations. BUT GPU preemption approaches incur variable and high latency because:
Rely on existing CUDA thread blocks or Slice tasks to provide pre-emption points
  Rare preemtion points incur high latency, while frequent pre-emption points increase task execution time.
Store stopped task’s state
  Save the pre-empted task state in the GPU memory can lead to memory monopolization for tasks with large memory footprint
  While saving task state to host memory introduces variable latency.
BUT high preemption latency affects violations.
As you can see in the figure, (click)
we send the stop signal (click)

## Slide 4: Preemption can reduce SLA violations
GPU preemption approaches incur variable & high latency:
1. Rely on existing thread blocks or slice tasks to provide preemption points
  Rare preemption points  high latency
  Frequent preemption points  increase task execution time
2. Store stopped task’s state
  In GPU memory  memory monopolization
  In Host memory  variable latency
High preemption latency affects violations
Time
SLA
B
Stop signal
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Task stopped
B
Preemption latency
Notes: BUT the batch task, can NOT stop immediately, for the reasons mentioned before. (click)
The time between we sent the stop signal and the time that a task actually stops is called preemption latency. (click)

## Slide 5: Preemption can reduce SLA violations
GPU preemption approaches incur variable & high latency:
1. Rely on existing thread blocks or slice tasks to provide preemption points
  Rare preemption points  high latency
  Frequent preemption points  increase task execution time
2. Store stopped task’s state
  In GPU memory  memory monopolization
  In Host memory  variable latency
High preemption latency affects violations
Time
SLA
B
Stop signal
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Task stopped
B
Preemption latency
U
We need preemption mechanism with constant & low latency
  Much shorter than the SLA
Notes: If the preemption latency is high the user-facing tasks will violate the SLA. (click)
As a result we need a preemption mechanism with constant and low latency much shorter than the SLA

## Slide 6: TReM: Task Revocation Mechanism for GPUS
With constant & low latency
To achieve that TReM:
  Stops a task at any point of its execution  low & constant latency
  Does not store the state of the revoked task  constant latency
  Replays the revoked task later
To stop a task TReM uses 3 mechanisms
  CUDA dynamic parallelism
  CUDA unified memory
  asm(trap)
We examine the effectiveness of TReM on SLA violations
  Using different scheduling policies
  Focusing on long running batch tasks (i.e. execution time relative to SLA)
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Notes: In this work we present TREM; A task revocation mechanism with constant and low latency.
To achieve that TREM (a) Stops a task at any point of its execution, providing low and constant latency (b) Does not store the state of the revoked task, providing constant latency, and (c) Replays the revoked task later. (click)
The most challenging part is to stop a task from inside the GPU. To do so TREM uses three mechanisms: CUDA dynamic parallelism, CUDA unified memory, and Asm(trap). We are going to provide more details later.
We examine the effectiveness of TReM on SLA violations, using different scheduling policies, and we focus on GPU sharing among user-facing and long running batch tasks, with execution time close to SLA (click)

## Slide 7: Why TReM?
Desired features | FLEP | GPES | Pascal Preemption | Chimera | TReM
Preemption/Revocation | P | P | P | P | R
Provides Low & Constant preemption latency | - | - | - | + | +
Handles tasks with large memory footprint | - | - | + | + | +
Does not need kernel source code | - | - | + | - | +
Supports all NVIDIA GPUs | + | + | - | + | +
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Notes: In this table we compare State of the art preemption approaches as FLEP, GPES, Pascal Compute preemption, and Chimera, with TREM.
For the comparison we use the following features: (Click)
  The existence of a Preemption or Revocation support. The difference between preemption and revocation is that preemption saves the stopped task’s state. TREM supports revocation. (Click)
  While all the other approaches support preemption.
  (2xClick)
  The next feature focus in the latency of the preemption mechanism. The revocation mechanism of TREM provides low and constant overhead because it can stop a kernel at any point of its execution and does not store any state either in the host or GPU memory. (Click)
  On the contrary preemption approaches as FLEP, GPES and Pascal Compute preemption can NOT provide constant overhead because they can stop a kernel at certain points of its execution and store the state of the preempted task.
  (2xClick)
  The third feature is about the ability of the approach to handle tasks with large memory footprint. TREM is able to handle tasks with large memory footprint because it does not store the revoked task state to the GPU memory, (Click) opposed to FLEP and GPES.
  (2xClick)
  The forth one focus in the kernel source code and if it requires modifications to support preemption. TREM does not need modifications to the kernel source code because it works with CUDA dynamic parallelism. (Click)
  Again FLEP and GPEs require the kernel source code in order to add preemption points
  (2xClick)
  The fifth one is about the ability of the approach to function with all NVIDIA GPUs. TREM works with NVIDIA GPUs that support CUDA dynamic parallelism, which are GPUs with compute capability greater than 3. GPUs with this compute capability are all of the state-of-the-art GPUs, except outdated FERMI architecture. (Click)
  On the other hand Pascal compute preemption works with only Pascal architecture.
TREM in the only approach that has all the above mentioned features

## Slide 8
TReM Design Overview
Notes: Now we are going to TREM Design

## Slide 9: TReM components
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Host
GPU
Host memory
GPU memory
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
Wrapper kernel
Actual kernel
Unified memory
Context
p2
Revoke flag
Context
p1
Process
Pool
p1
p2
TReM
Notes: In this figure we see the basic components of TREM that exist in Host and GPU. In the left part of the figure we see the Host (click) while in the right the GPU(click).
In the Host we see a pool of processes.
In the GPU we see the wrapper kernel which uses one CUDA core. This wrapper kernel spawns the Actual kernel in the remaining CUDA cores by the use of CUDA dynamic parallelism.
In the GPU memory we can see that we have two pre-initialized CUDA contexts of the processes in the Process pool.
Moreover, we see the revoke flag variable allocated in the Unified memory, which is a common address space between the GPU and the host. Both Host and GPU can read and write this variable. (click)

## Slide 10: Overall system with TReM
Apps
Host
GPU
Host memory
GPU memory
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
Wrapper kernel
Actual kernel
Unified memory
Context
p2
Revoke flag
Context
p1
TReM
Task
Queues
Process
Pool
p1
p2
Runtime
framework
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Notes: In this figure we see the overall runtime system and the place of TREM in it (click)
Applications are in the left part of the figure and (click) contain tasks. (click)
Then we have task queues used from applications. (click)
And finally we have the runtime framework. (click)

## Slide 11: Start a kernel with TReM
Host
GPU
Host memory
GPU memory
Process
Pool
p1
p2
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
Wrapper kernel
Actual kernel
Unified memory
Context
p2
Revoke flag
Context
p1
TReM
Task
Queues
push
Apps
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Runtime
framework
Using CUDA Dynamic Parallelism
Notes: Now we are going to see how we start a kernel with TREM (click) using CUDA Dynamic Parallelism (click)
Apps uses (click) task queues to push their tasks.

## Slide 12: Start a kernel with TReM
Host
GPU
Host memory
GPU memory
Process
Pool
p1
p2
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
Wrapper kernel
Actual kernel
Unified memory
Context
p2
Revoke flag
Context
p1
TReM
Task
Queues
push
pop
send
launch
issue
poll
Apps
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
p1
Context
p1
Runtime
framework
Notes: The runtime framework selects a task queue according to a scheduling policy and (2xclick) pops the first task.
Then the framework (click) sends it to (click) the active process in the process pool. The context of this process becomes active in the GPU memory.
The active process launches the wrapper kernel (click)
And the wrapper kernels issues (click) the actual the kernel, using CUDA dynamic parallelism, and starts (click) polling the revoke flag, allocated in the Unified memory. (click)

## Slide 13: Revoke a kernel with TReM
Host
GPU
Host memory
GPU memory
Process
Pool
p1
p2
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
Wrapper kernel
Actual kernel
Unified memory
Context
p2
Revoke flag
Context
p1
TReM
Apps
Task
Queues
asm(trap)
detect
set
kill
detect kernel stop
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Context
p1
unusable
Runtime
framework
Using asm(trap)
Notes: Now we are going to see how we stop a kernel with TREM (click) using asm(trap). (click)
  The framework sets the revoke flag
  The wrapper kernel detects (click) that the revoke flag is set and (click) calls asm(trap). Asm(trap) is normally called when a kernel code assertion fails.
  The Actual kernel Is (click) killed and
  The context of the active process becomes (click) unusable due to the asm(trap).
  The framework detects (click) that that the kernel had stopped and marks (click) the active process as unusable.

## Slide 14: Revoke a kernel with TReM
Host
GPU
Host memory
GPU memory
Process
Pool
p1
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
Wrapper kernel
Actual kernel
Unified memory
Context
p2
Revoke flag
Context
p1
TReM
Apps
Task
Queues
unusable
Context
p2
pop
issue
p2
send new task
p2
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
poll
launch new wrapper
Runtime
framework
Notes: In order to start a new task.
  The framework pops (click) a new task lets say from the next task queue (click)
  Sends (click) the task to the next active process
  Then the active process launches (click) the new wrapper which issues (click) the actual kernel.
  And the wrapper kernel (click) starts polling the revoke flag. (click)

## Slide 15: TReM breakdown
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Revocation time = 22ms
  To stop the task: 5 ms
  To start the new task: 17 ms
Book-keeping time = 75 ms
  Postponed until next batch task
Time
B
Time
Set Revoke flag
B
Start user facing
U
U
Revocation latency =22ms
U
U
Replenish
process
Clear context =60ms
New process
=15ms
Book-keeping =75ms
Clear
context
Restart
batch
B
  To clear the GPU context: 60ms
  To replenish the process pool: 15ms
Notes: In this slide we are going to see the breakdown of TREM’s latency
The first figure shows the timing of an execution without pre-emption, as we have seen in previous slides. The user-facing will wait for the batch task to finish, in order to start executing.
The second figure presents the timing of TREM
We need 22 ms from the time set the revoke flag until we start the next task, this the revocation latency. If we break it down we need 5ms to stop the currently executing task and another 17ms to start the next task. The 5ms are spent to set and read the revoke flag in the unified memory and to detect that the kernel had stopped. The 17ms are spent in the first CUDA call.
We spend on Book-keeping 75ms, if the next task is batch.
In particular, we need 60 ms to clear the unusable GPU context of the previous active process, and 15 ms to replenish the process pool. We need to have at least two processes in the pool to fulfill the case that, a batch is executed and we decide to kill it And immediately serve user-facing tasks. These 75 ms are postponed until the next batch task so they do not affect the user-facing response time.

## Slide 16: TReM with multiple GPUs
Servers today
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Runtime
framework
TReM
p1
TReM
p1
Task
Queues
GPU
GPU
Apps
In such setups TReM runs in every GPU
  Have multiple GPUs & run multiple applications
To handle multiple GPUs & apps
  We design & implement a runtime framework
The runtime framework
  Instructs TReM when to revoke a kernel
  Minimize lost work due to revocations
  Selects which task queue to serve according to a scheduling policy
We use two scheduling policies:
  (Baseline) Priority: Prioritizes user-facing over batch tasks
  Elastic: Packs user-facing tasks in a GPU  do not violate the SLA
    Devotes the remaining GPUs to batch tasks
Notes: Servers today
Have multiple GPUs and run multiple applications, that use queues to push their tasks, as you can see in the fig on the right (click)
In a Multiple GPU setup TREM runs in every GPU. For simplicity we have one process in the process pool. (click)
To handle multiple GPUs and applications we have design and implement a runtime framework. (click)
The runtime framework
  Instructs TREM when to revoke a kernel, minimize the lost work due to revocations, because they select to revoke the shortest task first, finally it selects which task queue to serve according to a scheduling policy (click)
We use to scheduling policies: Priority as Baseline. It just Prioritizes user-facing over batch and it does not have any knowledge about SLA. Moreover, we have design and implement Elastic, which packs user-facing tasks in a GPU, as such they do not violate the SLA, and devotes the remaining GPUs to batch tasks.

## Slide 17: Priority vs Elastic scheduling policy
Scheduler
pop
pop
send
send
Task
Queues
GPU
GPU
B
U
U
B
B
Priority
Elastic
Does not account the user-facing latency
Scheduler
pop
send
Task
Queues
GPU
GPU
B
U
U
B
B
send
pop
Assigns the minimum number of GPUs
  As such user-facing response time < SLA
  In our example 1xGPU is sufficient
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Assigns all GPUs to user-facing
  As many as the number of user-facing tasks
Postpones the execution of batch tasks
Provides the remaining GPUs to batch tasks
Notes: Now we are going to compare Priority and Elastic scheduling policy. In this figure we have a multi-GPU setup, with TREM running in each GPU, the scheduler that spawns one thread per GPU, and task queues with user-facing and batch tasks.
(click)
Priority does not account the user-facing latency and has no notion about the SLA. It just prioritizes user-facing over batch tasks. (click)
So it assigns as many GPUs to user-facing, as the number of pending user-facing tasks in the system. In our example the two user-facing tasks of the first task queue will be send to two GPUs (click)
And batch tasks are postponed. (click)
Elastic assigns the minimum number of GPUs to user-facing tasks, (click)
As such they meet their SLA target. (click)
Lets assume that one GPU is sufficient to satisfy the imminent user-facing load, (click)
so Elastic will send all user-facing tasks from the first task queue to the first GPU (click)
The remaining GPUs will be used from batch tasks. (click)

## Slide 18: Priority vs Elastic scheduling policy
Scheduler
pop
pop
send
send
Task
Queues
GPU
GPU
B
U
U
B
B
Priority
Elastic
Wait for the currently executing user-facing
Assigns the GPUs to new user-facing
Postpones the execution of batch tasks
Scheduler
pop
send
Task
Queues
GPU
GPU
B
U
U
B
B
When the user-facing load increases
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
send
pop
Elastic assigns more GPUs for user-facing
  In our example 1xGPU is sufficient
U
U
U
U
pop
Batch tasks are postponed
Notes: As the load of user-facing tasks increases.
Priority will wait for the currently executing user-facing task to finish and then it will assign the two GPUs to the newly arrived user-facing tasks. Again the execution of batch tasks is postponed.
Elastic assigns more GPUs to user-facing tasks. In our example lets assume that with one MORE GPU, the response time of user-facing tasks will be smaller than the SLA. As a result, the scheduler will select the second queue to pop tasks and send them to the second GPU.
Batch task execution will be postponed. However, without TREM we should wait for the batch task to finish before we can provide the GPU to the user-facing tasks

## Slide 19: Incorporating TReM in Priority & Elastic
Scheduler
pop
pop
send
send
Task
Queues
TReM
GPU
p1
TReM
GPU
p1
B
B
B
Priority
Elastic
Initially there are no user-facing tasks
  All GPUs are provided to batch
Scheduler
pop
pop
send
send
Task
Queues
TReM
GPU
p1
TReM
GPU
p1
B
B
B
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Notes: Now we are going to see how TREM is intergraded with Priority and Elastic in order to stop the current executing batch task.
Initially there are now user-facing tasks in the system so all GPUs are provided to batch tasks

## Slide 20
Scheduler
pop
pop
send
send
Task
Queues
TReM
GPU
p1
TReM
GPU
p1
B
B
B
Priority
Elastic
  Priority revokes both GPUs
Initially there are no user-facing tasks
  All GPUs are provided to batch
A burst of user-facing arrives
Scheduler
pop
pop
send
send
Task
Queues
TReM
GPU
p1
TReM
GPU
p1
B
B
B
U
U
U
U
  Elastic revokes one GPU
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Incorporating TReM in Priority & Elastic
Notes: Then a burst of user-facing tasks arrives
Priority will revoke both GPUs because it is going to spread the user-facing tasks.
On the other hand elastic recognizes that one GPU can serve the user-facing. So it revokes only the first one.

## Slide 21
Scheduler
pop
pop
send
send
Task
Queues
TReM
GPU
p1
TReM
GPU
p1
B
U
U
B
B
Priority
Elastic
  Both GPUs are provided to user-facing
Initially there are no user-facing tasks
  All GPUs are provided to batch
A burst of user-facing arrives
Scheduler
pop
send
send
Task
Queues
TReM
GPU
p1
TReM
GPU
p1
B
B
B
U
U
  1 GPU is provided to user-facing
pop
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Incorporating TReM in Priority & Elastic
Notes: In Priority both user-facing will start executing to two GPUs.
In Elastic only one GPU is provided to user-facing while the remaining are used from batch.

## Slide 22
Experimental Methodology

## Slide 23: Testbed
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
We use a server with:
  Intel Xeon CPU E5-2630 v3 running at 2.40GHz
  128GB of DRAM
  4xNVIDIA P1000 GPUs (Pascal Architecture)
Each GPU
  Has 640 CUDA cores & 4GB of GDDR5
  Connected with a 16 lanes PCIe gen3
We use CUDA 9.0 to implement TReM

## Slide 24: Workloads
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Micro-benchmarks
  With a few tasks
  To measure the overheads of TReM
Datacenter-inspired synthetic workloads
  With thousands of user-facing & batch tasks
  To measure the performance of the overall system
We use tasks from Rodinia 3.2 and NVIDIA SDK
Tasks | AVG Exec. Time (ms) | Memory Footprint (MB)
Euclid | 8 | 12
NW | 38 | 44
Pathfinder | 68 | 74
Monte Carlo | 150 | 68
Lava MD | 46000 | 1069
Hot Spot | 130696 | 423
Gaussian | 311000 | 1120
SLA = 200ms
  Tasks with execution time < SLA  user-facing
  Tasks with execution time >> SLA  batch
  user-facing
batch
Notes: We use to type of workloads to evaluate our system:
  Micro-benchmarks
    With a few tasks in order to measure the overhead of TREM
  And DC inspired synthetic workloads
    With thousands of user-facing & batch tasks, to measure the overall system performance
We use tasks from Rodinia 3.2 and NVIDIA SDK of CUDA toolkit 9.
You can see some of the tasks used in our evaluation in the table on the right. As you can observe we have execution times ranging from a few ms up to hundreds of seconds.
Moreover, we have tasks with memory footprint from MBs up to GBs
We consider the SLA to be 200ms according to previous approaches.
Tasks with execution time < SLA are user-facing while tasks with execution time >> SLA are batch

## Slide 25: Datacenter workloads
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
We implement a workload generator
  Mimics traces from Google and Alibaba
  Takes 3 parameters:
    Job duration  Pareto distribution
    Job inter-arrival time  Exponential distribution
    User-facing to batch job ratio  50:50 (Alibaba), 80:20 (Google)
We generate two workloads: W1 & W2
Workload specs | W 1 | W 2
User-facing to batch ratio | 50:50 | 80:20
User-facing job duration (mean) | 5s | 
Batch job duration (mean) | 600s | 
Total # of jobs | 30 | 
Total # of tasks | 1560 | 
Notes: To generate the datacenter-inspired workload we implement a workload generator that mimics traces from Google and Alibaba
Our workload generator takes 3 parameters:
  Job duration that follows pareto distribution (click)
  Job inter-arrival time that follows an exponential distribution (click)
  And User-facing to batch job ratio: fifty-fifty according to Alibaba and eighty-twenty according to google (click)
We generate two workloads Workload 1 and 2. As you can see in the table on the right corner.
  The two workloads differ in the user-facing to batch ratio.
  The user-facing job duration mean and the batch job duration mean is the same for both workloads
  The same happens with the total number of tasks and jobs

## Slide 26: Datacenter workloads
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
We implement a workload generator
  Mimics traces from Google and Alibaba
  Takes 3 parameters:
    Job duration  Pareto distribution
    Job inter-arrival time  Exponential distribution
    User-facing to batch job ratio  50:50 (Alibaba), 80:20 (Google)
We generate two workloads: W1 & W2
To emulate different Load
  We use a scaling factor on the base inter-arrival mean
  The scaling factor ranges from 0.25 (low load) to 2.0 (oversubscription)
    Load 0.25 can fully utilize one GPU
    Load 1 can fully utilize four GPUs
Workload specs | W 1 | W 2
User-facing to batch ratio | 50:50 | 80:20
User-facing job duration (mean) | 5s | 
Batch job duration (mean) | 600s | 
Total # of jobs | 30 | 
Total # of tasks | 1560 | 
Load | 0.25 - 2 | 
Notes: To emulate different load we use a scaling factor on the base inter-arrival mean. Effectively, the scaling factor modifies the density of job arrivals, and as a result, the load and the burstiness of the workload
The scaling factor ranges from 0.25 which is a low load up to 2.0 which is oversubscription
  Load 0.25 can fully utilize temporally a GPU
  Whereas Load1 can fully utilize 4 GPUs
More information about the workload generator can be found in our paper

## Slide 27
Experimental Analysis
Notes: Now we are going to move to our experimental analysis.

## Slide 28: SLA violations
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
W1: 50% user-facing – 50% batch
W2: 80% user-facing – 20% batch
≈ 8%
≈ 10%
Notes: These plots show the percentage of tasks meeting the SLA for all scheduling policies Priority, Elastic, Priority+TREM and Elastic+TREM.
X-axis shows the load and spawns from low load (0.25) up to oversubscription(2.0). Y-axis shows the percentage of tasks that meet the SLA. We have the same plot for both Workloads; W1 and W2.
At low load 0.25 there is no much resource contention so there is no difference between policies with and without Trem in both workloads
As the load increase, the difference between Tasks meeting the SLA, between policies with and without TReM increases rapidly, in both Workloads.
In Particular, in W1 the difference in oversubscription is 8%, whereas in W2 is 10%. The difference in W1 and W2 is due to the fact that in W2 we have more user-facing tasks at runtime so we use more the revocation mechanism

## Slide 29: Lost work due to revocations
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Chart: Load
| 0.25 | 0.5 | 1 | 2
Elastic+TReM | 1.1 | 1.9 | 2.1 | 2.7
Priority+TReM | 1.8 | 2.3 | 3 | 3.3
0,6%
0,7%
Both policies minimize wasted time
  Revoke more recently started tasks
Elastic minimize more wasted time
  Uses minimum # GPUs for user-facing
Notes: TReM in order to provide low revocation latency it does not store the state of the pre-empted task, hence the batch task starts from the beginning. In this Figure we see the lost work due to revocations. The x-axis shows the load, whereas the y-axis the wasted time due to revocations. The wasted time represents the work that need re-execute due to revocations.
As we observe the wasted time increases as the load increases from low to oversubscription. (Click) At low load (0.25), the wasted time percentage for both Elastic and Priority is below 2%, while at load 2.0 it reaches 3%. Both policies, Priority and Elastic minimize this amount of wasted work because choose to revoke the batch task that has started most recently.
Moreover, Elastic has on average 0,6% less wasted work than Priority. This happens because Elastic performs less revocations, because it uses the minimum amount of GPUs in order to satisfy the user-facing load and also because it will revoke a batch task only if its remaining time is less than the revocation overhead.

## Slide 30: PDF with batch job duration
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Chart: Job Percentile (%)
| 0 | 15 | 30 | 50 | 70 | 85 | 100
Elastic | 80.5 | 82 | 86 | 104.9 | 134.2 | 134.6 | 134.7
Elastic+TReM | 110 | 134.1 | 138.7 | 145.5 | 214.3 | 265 | 291
94%
30%
Notes: This Figure depicts time to completion for batch jobs running under Elastic with and without TREM. The x-axis shows the job percentile, while the y-axis the time to completion in seconds. As expected, time to completion of batch jobs increases with TReM because tasks are revoked and replayed. Time to completion increases from 30% up to 94%.

## Slide 31: Compare revocation mechanisms
 |  | Latency (ms) |  | 
Kernel dimensions | Total threads | Process kill | asm(exit) | asm(trap)
Kernel <16,16> | 256 | 3000 | 130 | 22
Kernel <32,32> | 1024 | 3000 | 195 | 22
Kernel <64,64> | 4096 | 3000 | 600 | 22
Kernel <128,128> | 16384 | 3000 | 1430 | 22
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
+ Constant latency
- High latency
Process kill:
Notes: In this slide we are going to evaluate the 3 ways that exist in order to stop a kernel and we are going to answer why the asm(trap) is selected for TREM.
These 3 ways to stop a kernel are:(click)
  Kill the issuing process on the host named as process kill (click)
  Use asm(exit) which is normally called when a kernel uses return (click)
  Use asm(trap) which is normally called when a kernel code assertion fails (click)
But each method implies different latency.
(click)
We are going to compare the latency in ms of these three mechanism, with varying kernel dimensions. The first column, SHOWS the cuda threads and blocks used in each kernel. The second column, PRESENTS the total number of threads spawned in each kernel
(click)
The first approach, process kill, has a constant but high latency, which approximates 3 seconds. This happens because the NVIDIA driver clears the killed kernel’s context and prepares the CUDA environment to be functional again.

## Slide 32: Compare revocation mechanisms
 |  | Latency (ms) |  | 
Kernel dimensions | Total threads | Process kill | asm(exit) | asm(trap)
Kernel <16,16> | 256 | 3000 | 130 | 22
Kernel <32,32> | 1024 | 3000 | 195 | 22
Kernel <64,64> | 4096 | 3000 | 600 | 22
Kernel <128,128> | 16384 | 3000 | 1430 | 22
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
- Variable latency
asm(exit):
- High latency
Notes: The second approach, asm (exit), has a variable latency which (click) increases as the number of threads increase. This is because the GPU must wait for all threads of the kernel to exit.
(click)
Typically, kernels launch thousands of threads , which can incur a delay of several seconds. And as we can see a kernel with more than sixteen thousand threads has a latency that approximates 1.5s

## Slide 33
 |  | Latency (ms) |  | 
Kernel dimensions | Total threads | Process kill | asm(exit) | asm(trap)
Kernel <16,16> | 256 | 3000 | 130 | 22
Kernel <32,32> | 1024 | 3000 | 195 | 22
Kernel <64,64> | 4096 | 3000 | 600 | 22
Kernel <128,128> | 16384 | 3000 | 1430 | 22
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
+ Constant latency
+ Low latency
asm(trap):
TReM uses asm(trap)
Compare revocation mechanisms
Notes: Finally asm(trap) (click) has a constant and low latency that is 22ms. (click)
For those reasons we select asm(trap) to stop a kernel in TREM .

## Slide 34: SLA violations vs. Revocation latency
Chart: Revocation latency (ms)
| 3200 | 1600 | 800 | 400 | 200 | 40 | 20 | 10
Elastic+TReM | 8 | 7 | 6 | 4.3 | 3.7 | 3 | 2 | 1.5
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Notes: In this figure we simulate different revocation latency varying from 10 and 1000ms for Elastic with TREM. The x-axis shows the revocation latency, while the y-axis the percentage of tasks violating the SLA. The percentage of violations decrease as the revocation latency diminishes. (click)
To ensure the SLA for 99% of user-facing tasks we need a revocation mechanism with less than 10ms latency.

## Slide 35
Conclusions
Notes: To conclude

## Slide 36: TReM: A Task Revocation Mechanism for GPUs
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
To provide QoS under GPU sharing
  We need a preemption or revocation mechanism
BUT this mechanism should have constant and low latency (<<SLA)
TReM is a Task Revocation Mechanism
  Stops a kernel at any point of its execution without storing state
  Replays the revoked task later
TReM revocation latency is 22ms
TReM + Elastic
  Ensure the SLA for 8% more user-facing tasks compared to Priority
  Limits the lost work due to revocations to 2,1% on average
Notes:   To provide QoS under GPU sharing we need a preemption or revocation mechanism. BUT the preemption or revocation mechanism should have constant and low latency
  TREM is a Task Revocation Mechanism that
    Stops a kernel at any point of its execution without storing the state of the stopped task
    And replays the revoked task later
  TREM requires 22ms to stop a task and start the next one.
  TREM integrated with Elastic ensure the SLA for 8 percent more user-facing tasks when collocated with long running batch tasks compared to Priority without TREM
  Also TREM limits the loss of useful work due to revocation to 2,1% on average across all loads.

## Slide 37
Thank you
Manos Pavlidakis
manospavl@ics.forth.gr
Questions?
Notes: Thank you very much for you attention I will be happy to answer any questions.

## Slide 38: SLA violations
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
W1: 50% user-facing – 50% batch
W2: 80% user-facing – 20% batch
≈ 0,8%
≈ 0.4%
Notes: By comparing Priority and Elastic at oversubscription load in W1 we observe that with Priority (click) 0.4 percent more tasks meet their SLA. (click)
In W2 the difference in slightly higher and approximates 0,8%.
This happens because Priority utilizes all GPUs to handle user-facing load, which results in significantly more revocations as we are going to see next. On the contrary Elastic aims to decrease the number of revocations without increasing much SLA violations.
We have performed experiments with more GPUs and different revocation latencies but more information can be found in our paper

## Slide 39: Batch job duration
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Chart: Job Percentile (%)
| 0 | 15 | 30 | 50 | 70 | 85 | 100
Priority | 79 | 81 | 87 | 105.2 | 134.2 | 134.3 | 134.8
Priority+TReM | 134.1 | 139 | 142 | 177 | 268 | 284 | 421
Notes: This Figure depicts time to completion for batch jobs for Priority scheduling policy.
The x-axis shows the job percentile, while the y-axis the time to completion in seconds.
As expected, time to completion of batch jobs increases with TReM because tasks are revoked and replayed.

## Slide 40: Batch job duration
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Chart: Job Percentile (%)
| 0 | 15 | 30 | 50 | 70 | 85 | 100
Priority | 79 | 81 | 87 | 105.2 | 134.2 | 134.3 | 134.8
Priority+TReM | 134.1 | 139 | 142 | 177 | 268 | 284 | 421
1.6x
3.2x
Notes: In particular for 50% of the jobs, Priority+TReM has 1.6 times higher time to completion compared to simple Priority.
For greater percentiles, Priority+TReM has 3,2 times higher time to completion compared to simple Priority

## Slide 41: Batch job duration
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Chart: Job Percentile (%)
| 0 | 15 | 30 | 50 | 70 | 85 | 100
Elastic | 80.5 | 82 | 86 | 104.9 | 134.2 | 134.6 | 134.7
Elastic+TReM | 110 | 134.1 | 138.7 | 145.5 | 214.3 | 265 | 291
Notes: This is the same Figure as before BUT now it is for Elastic scheduling policy.
Again, time to completion of batch jobs increases with TReM because tasks are revoked and replayed.

## Slide 42: Batch job duration
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Chart: Job Percentile (%)
| 0 | 15 | 30 | 50 | 70 | 85 | 100
Elastic | 80.5 | 82 | 86 | 104.9 | 134.2 | 134.6 | 134.7
Elastic+TReM | 110 | 134.1 | 138.7 | 145.5 | 214.3 | 265 | 291
1.3x
2.1x
Notes: For 50% of the jobs Elastic+TReM exhibits 1.3 times increase in time to completion compared to Elastic without TREM
For greater percentiles, Priority+TReM has 2,1 times higher time to completion compared to Elastic

## Slide 43: Scalability of TReM
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Chart: Number of GPUs
| 1 | 2 | 4 | 8 | 16 | 32
Elastic | 12.23 | 12.01 | 5.21 | 1.53 | 0.61 | 0.61
Elastic+TReM | 10.98 | 2.16 | 0.98 | 0.65 | 0.63 | 0.63
Chart: Revocation latency (ms)
| 10 | 20 | 40 | 200 | 400 | 800 | 1600 | 3200
Elastic | 5.8 | 5.8 | 5.8 | 5.8 | 5.8 | 5.8 | 5.8 | 5.8
Elastic+TReM | 0.5 | 0.9 | 1.9 | 2.6 | 3.2 | 4.5 | 5.6 | 6.9
asm(exit)
process kill
Notes: To evaluate our system with more than four GPUs and different revocation latencies, we implement a simulator. Our simulator models Elastic with and without TReM.
It takes as parameters (1) the task execution time, (2) the workload, and (3) the revocation latency.
In these experiments we run W1 and W2 for load 1.0 with simple Elastic and Elastic integrated with TREM.
In the figure on the left side, the x-axis shows the number of GPUs, while y-axis the percentage of tasks that violate the SLA.
In this experiment we vary the number of GPUs between 1 and 32. We see that using TReM we achieve 1 percent violations with 4 GPUs,
whereas without TReM we need 16 GPUs to achieve the same percentage.
In the figure on the right side the x-axis shows the revocation latency, while the y-axis the percentage of tasks violating the SLA.
In this experiment we vary the revocation latency between 10 and 1000 ms. The percentage of violations increases proportionally with revocation latency.
Consequently, other mechanisms such as asm(exit) and process kill that introduce 1,5 and 3 seconds latency can meet SLA for approximately 94% of user-facing tasks.
To ensure SLA for more than 99% of user-facing tasks, we require a revocation mechanism with 10ms latency.

## Slide 44: GPU allocation with Elastic
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Notes: This figure shows how elastic partitions GPUs to user-facing and batch tasks.
The upper part of the figure shows the number of GPUs allocated to user-facing tasks and the number of GPUs used to run batch tasks.
The lower part of the figure depicts the actual latency of user-facing tasks over time.
When user-facing tasks arrive (red crosses in the lower part), Elastic allocates more GPUs to user-facing tasks to avoid SLA violations.

## Slide 45: Overall system + TReM
Apps
Host
GPU
Host memory
GPU memory
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
Wrapper kernel
Actual kernel
Unified memory
Context
p2
Revoke flag
Context
p1
TReM
Task
Queues
Process
Pool
p1
p2
Scheduler
TReM: A Task Revocation Mechanism for GPUs
HPCC 2020
Notes: Now we are going to see how we start a kernel with TREM
Applications are in the left part of the figure and contain tasks. Then we have task queues used from applications. And finally we have the runtime scheduler.