## Slide 1
Stelios Mavridis, Manos Pavlidakis, Ioannis Stamoulias, Christos Kozanitis, Nikos Chrysos, Christoforos Kachris, Dimitrios Soudris, and Angelos Billas
Simplifying Software Access and Sharing of FPGAs in Datacenters
Notes: I am going to present to you vinetalk a framework that simplifies software accesses and provides FPGA sharing in Datacenters

## Slide 2
Difficult to write Host code for single & different accel. type(s)
  Accelerator code and Host code are currently tightly coupled
    Results in increased programming effort for application developer
    Reduced accelerator code reuse
    Requires detailed programming knowledge for Host & Accelerator side
Difficult to share the same IP core from multiple apps
  Typically IP cores are dedicated
  But in consolidated servers sharing is important
Difficult to use multiple accelerators from one app
  Host code has to change significantly
Challenges for using accelerators in servers
Notes: Today the typical mode of using accelerators in servers is presented at the figure. This mode introduces three main challenges…
From one developer

## Slide 3
VineTalk: Software layer between FPGAs & apps
3
VineTalk addresses the pre mentioned issues
  Host code and FPGA code is decoupled
    Host code is written once, regardless of the accelerator number & type
  Provides IP core sharing from multiple applications
  Apps can use multiple/heterogeneous accelerators
VineTalk supports VMs, Native, and Containers
VineTalk consists of two main components
  Transport protocol
  Extensive scheduling
VineTalk virtualizes accelerators

## Slide 4
VineTalk’s design
Transport layer
  Implemented as shared memory
    Enables VMs & Containers
    Faster than network approaches
  Virtual Accelerators
    Implemented as task queues
    Allows FPGA sharing
Accelerator Controller
  Schedules multiple apps over a single accelerator
  Schedules one app over multiple accelerators
  Schedules one app over heterogeneous accelerators
4
Single Server
Notes: The share memory in consolidated servers is the faster than network approaches
Accelerator controller basically schedules and executes tasks in the physical accelerators

## Slide 5
Preliminary evaluation
5
Perform risk analysis
  With three financial apps with & without VineTalk
  Black&Scholes, Black-76, and Bionomial
Question 1: Is VineTalk expensive ?
  Up to 4% slower compared to native execution
Question 2: Is FPGA sharing expensive ?
  With 2 concurrent apps
  2% less task rate compared to 1 app running standalone
Programming effort
  Decrease the lines of Host code up to 30% compared to native
  Accelerator specific code moved to Accelerator Controller
Notes: We examined the basic overhead of vinetalk and if FPGA sharing introduces significant overhead. To do that we performed Risk Analysis , with three …
We reduced the programing effort because we decrease the line of the Host code up to 30% compared to native implementation
This accelerator specific code is moved to the Accelerator Cotroller

## Slide 6
Thank you! Questions?
Summary
6
VineTalk virtualizes heterogeneous accels. in consolidated servers
  Using one efficient transport layer and an Accelerator Controller
  The Accelerator Controller provides task scheduling and FPGA sharing
Benefits of VineTalk
  Accelerator sharing
  Host code is written once
  Apps can be executed in a Single/Multiple/Heterogeneous accelerators
  Apps can run in VMs, Natively, and in Containers
Our preliminary results show low overhead in simple case